## Slide 1
DESIGNED BY IBOTU
VITO
RAY
HEY
WAKE UP!
DO SOME
THINGS!
DESIGNED BY IBOTU
3-C
Han Jiarui, Song Junni, Liu Yahui, Chai Haochen, Zhang Youzhi
Smart Jump Rope for Cardio Workout

## Slide 2
DESIGNED BY IBOTU
VITO
RAY
HEY
WAKE UP!
DO SOME
THINGS!
DESIGNED BY IBOTU
Contents
01
02
03
04
Introduction
Aims and Objectives
Background
Materials and methods
05
06
Conclusion
Disscussion

## Slide 3
DESIGNED BY IBOTU
VITO
RAY
HEY
WAKE UP!
DO SOME
THINGS!
DESIGNED BY IBOTU
Introduction
PART .01

## Slide 4
PART.01
VITO
RAY
Introduction to smart rope
Jumping rope is an effective aerobic exercise that can burn approximately 12 calories per minute for a person weighing 150 lbs (about 68 kg),[1]
Do not provide real-time workout data
Design a smart jump rope so that it can calculate the calories burned by jumping rope while recording data
[1] Kim, Y., and H. Shin, "Design and implementation of smart jump rope system using mobile and IoT technologies," International Journal of Smart Home, vol. 12, no. 3, pp. 25-34, 2018.

## Slide 5
DESIGNED BY IBOTU
VITO
RAY
HEY
WAKE UP!
DO SOME
THINGS!
DESIGNED BY IBOTU
Aims
and
Objectives
PART .02

## Slide 6
PART.02
VITO
RAY
Aims and Objectives
measures the number of jumps and calories burned
Jump rope enthusiasts:
Creating personalized fitness plans
Social interaction
Recovery patients:
Rehabilitation training
Monitoring health status

## Slide 7
DESIGNED BY IBOTU
VITO
RAY
HEY
WAKE UP!
DO SOME
THINGS!
DESIGNED BY IBOTU
Background
PART .03

## Slide 8
PART.03
VITO
RAY
Background
Skipping rope served as a traditional aerobic exercise method.
The first generation of smart jump ropes are capable of accurately measuring users' jump counts and frequencies.
Modern smart jump ropes can synchronize data with health monitoring devices or smartwatches, providing personalized fitness advice and training plans.

## Slide 9
DESIGNED BY IBOTU
VITO
RAY
HEY
WAKE UP!
DO SOME
THINGS!
DESIGNED BY IBOTU
Materials and Methods
PART .04

## Slide 10
PART.04
VITO
RAY
Arduino UNO
MPU 6050
LCD display
PPT模板 http://www.1ppt.com/moban/
Materials

## Slide 11
PART.04
VITO
RAY
Methods
1，UI & LCD
Automatically switches to the weight selection screen, where the user selects their weight category using the joystick.
The user confirms the selection by pressing the joystick button, entering the jump rope state.
In the jump rope state, the counter and timer start, and the LCD updates the data in real-time.
The user presses the joystick button to stop jumping, transitioning to the jump rope end state.
- In the jump rope end state, the LCD displays the jump count, elapsed time, calories burned, and BPM (jumps per minute).

## Slide 12
PART.04
VITO
RAY
Methods
2，algorithm for coordinate

## Slide 13
PART.04
VITO
RAY
Methods
2，algorithm for coordinate
Reference： Lionel Brits - Hand drawn in Inkscape by me，CC BY 3.0，https://commons.wikimedia.org/w/index.php?curid=3362239

## Slide 14
PART.04
VITO
RAY
Methods
2，algorithm

## Slide 15
PART.04
VITO
RAY
Methods
3，algorithm for angular acc
Z
Trans t

## Slide 16
PART.04
VITO
RAY
Methods
2，algorithm

## Slide 17
PART.04
VITO
RAY
Methods
3，algorithm for signal processing
the sliding window is used to analyze accelerometer data over a set number of samples, defined by WINDOW_SIZE (10 samples). The window collects the most recent accelerometer readings, and as new data comes in, the oldest data point is replaced. This moving subset of data is then used to calculate the mean and variance, helping to smooth out noise and detect significant events like jumps. The window "slides" forward with each new data point, continuously updating the analysis.
THES:
mean = 12.7475
variance = 13.798

## Slide 18
PART.04
VITO
RAY
Methods
3，Calorie
1.Base Calories Burned per Jump: Determine the base calories burned per jump (baseCaloriesPerJump) based on the body type.
2.Calculate Average, Maximum, and Minimum Forces: Assume the accelerometer data for X, Y, Z axes are AcX, AcY, AcZ.

## Slide 19
PART.04
VITO
RAY
Methods
3，Calorie

## Slide 20
PART.04
VITO
RAY
Methods
3，Calorie

## Slide 21
PART.04
VITO
RAY
Results & data annalists

## Slide 22
PART.04
VITO
RAY
mean = 12.7475
variance = 13.798
Acc = 97.67%
Results & data annalists

## Slide 23
DESIGNED BY IBOTU
VITO
RAY
HEY
WAKE UP!
DO SOME
THINGS!
DESIGNED BY IBOTU
Discussion
PART .05

## Slide 24
1
Implications
Motivation and Accountability
Health Monitoring
2
Strengths
Accuracy and Precision
Convenience
3
Limitations
Assumption of Homogeneity
Proper Usage
External Factors
Discussion
PART.05
VITO
RAY

## Slide 25
DESIGNED BY IBOTU
VITO
RAY
HEY
WAKE UP!
DO SOME
THINGS!
DESIGNED BY IBOTU
Conclusion
PART .06

## Slide 26
more sophisticated technology
Great effort by every member.
There are still outstanding issues that require resolution：
Personalization
the lack of accuracy in the calculation.
Conclusion
VITO
RAY

## Slide 27
DESIGNED BY IBOTU
VITO
RAY
HEY
WAKE UP!
DO SOME
THINGS!
DESIGNED BY IBOTU
THANKS
3-C
2024
A SIMPLE AND NICE TEMPLATE HOPE YOU LIKE BY VITO RAY